MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:						Skylink Flight Services

AIRCRAFT TYPE/ MANUFACTURER: 		Cessna 172L/ Cessna Aircraft Company

YEAR OF MANUFACTURE:			1970

AIRCRAFT REGISTRATION:			5Y-CDD

AIRCRAFT SERIAL NUMBER:			17259295

DATE OF REGISTRATION:				07 August 2013

NUMBER AND TYPE OF ENGINE: 		One Lycoming O-320-E2D

DATE OF OCCURRENCE:				30 May 2016

TIME OF OCCURRENCE:				1135

LOCATION OF OCCURRENCE: 	Wilson Airport, Taxiway E

TYPE OF FLIGHT: 					Aircraft was on ground taxiing to apron 1

NUMBER OF PERSONS ON BOARD: 		1 crew

INJURIES: 	Minor

NATURE OF DAMAGE: 	Substantial

CATEGORY OF OCCURRENCE:	Ground incident

PIC FLYING EXPERIENCE: 			135 hours

All times given in this report is Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

5Y-CDD in an inverted placement after the occurrence

REMARKS

At approximately 1200 on 30 May 2016, the Air Accident Investigation Division was notified of an occurrence at Wilson airport (HKNW).

The occurrence was a ground incident involving two aircraft; a DHC-8 and a Cessna 172. The DHC-8 was conducting engine ground runs at the compass swing base off taxiway E at Wilson airport. The Cessna was taxiing to Apron 1 via taxiway E after landing on runway 14.

The Cessna had taken off from Wilson airport approximately 1021 for a training flight in the local training area and some circuits with a student pilot as the sole occupant. After the circuits, the aircraft landed on runway 14 and was advised to exit via taxiway E and hold short of runway 07.

To access that position, the Cessna had to cross behind the DHC-8. ATC reported to have sighted the Cessna 172 being blown over shortly thereafter as it crossed behind the DHC-8.

The 172 flipped over and came to rest on its roof. At least one of the DHC-8 engines was reported to have been running at the time.

ATC then tried to contact the DHC-8 crew to advise them to shut down engine power so as to allow for rescue to be performed on the stricken Cessna and were initially unsuccessful. Eventually one of the first responders was able to make contact with the crew of the DHC-8 while on site within view of the flight deck.

Fire and ambulance were dispatched to the site and the student pilot evacuated for first aid. Fire tender sprayed the area around the stricken Cessna with foam to reduce any fire risk due to fuel spillage.

Investigation is in progress.

CHIEF INVESTIGATOR OF ACCIDENTS

13/06/2016