MINISTRY OF TRANSPORT AND INFRASTRUCTURE

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION DIVISION

PRELIMINARY REPORT

OPERATOR:						Karen Blixen Camp Properties Ltd

AIRCRAFT TYPE/ MANUFACTURER: 		Robinson R44 Raven II/ Robinson Helicopter Co.

YEAR OF MANUFACTURE:			2014

AIRCRAFT REGISTRATION:			5Y-REE

AIRCRAFT SERIAL NUMBER:			13757

DATE OF REGISTRATION:				3 March 2015

NUMBER AND TYPE OF ENGINE: 		One Lycoming IO-540-AE1A5

DATE OF OCCURRENCE:				18 January 2019

TIME OF OCCURRENCE:				1100

LOCATION OF OCCURRENCE: 	Dimbolil Dam, Finlay Tea Estate, Kericho County,

S 00° 23.016’ E 035° 19.394’

TYPE OF FLIGHT: 					General aviation

NUMBER OF PERSONS ON BOARD: 		Three

INJURIES: 	None/minor

NATURE OF DAMAGE: 	Substantial

CATEGORY OF OCCURRENCE:	Accident

PIC:							Marc Goss

PIC FLYING EXPERIENCE: 			PPL: ~1,000 hours on type

Times given in this report are Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

An earlier photo of the occurrence aircraft

REMARKS

At about 1430 on 18 January 2019, the Aircraft Accident Investigation Division became aware of an occurrence in a dam in Kericho County.

The investigator in charge was able to obtain the PIC’s telephone contacts the following day at 1144 and and a telephone interview was conducted at 1300. The contacts of the two other occupants were also obtained and telephone interviews conducted at 1400 and 1430 respectively.

The PIC states that he had departed from Mara North in the Masai Mara with two passengers and approximately 140 litres of Avgas fuel (about 2 hours 20 minutes endurance). He flew for about 35 minutes to Dimbolil dam that is within the Finlay Tea Estate in Kericho. The two passengers disembarked and he flew onwards for 10 minutes to Olengureone Forest Station as the sole occupant. He later flew back solo to Dimbolil arriving at around 0930. At approximately 1100, the PIC took off from a grassy field adjacent to the dam, with the two passengers on board.

He states that the helicopter failed to attain sufficient lift, and due to the surrounding obstacles, elected to go over the water surface of the dam in an attempt to attain lift. This was not successful and the pilot elected to ditch in the water.

The helicopter contacted the water surface gently in an upright attitude. The pilot states that he made a right cyclic input to slow the rotors by contacting them to the water surface. All the occupants were able to extricate themselves from the sinking helicopter and swim to safety. There were no injuries reported.

The investigation is in progress.

Kithinji N.M.

Investigator-In-Charge

21/01/2019