MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:						Ninety Nines Flying School

AIRCRAFT TYPE/ MANUFACTURER: 		Cessna 172K/ Cessna Aircraft Corporation

YEAR OF MANUFACTURE:				1969

AIRCRAFT REGISTRATION:				5Y-BXQ

AIRCRAFT SERIAL NUMBER:			17258317

DATE OF REGISTRATION:				19 January 2010

TYPE OF ENGINE: 					Lycoming 0-320-E2D

DATE OF OCCURRENCE:				02 May 2016

TIME OF OCCURRENCE:				1546

LOCATION OF OCCURRENCE: 	Wilson Airport left of Rwy 07, after Twy B

TYPE OF FLIGHT: 					Commercial (Training)

NUMBER OF PERSONS ON BOARD: 		 1

INJURIES: 	None

NATURE OF DAMAGE: 	None

CATEGORY OF OCCURRENCE:	Serious incident

PIC’S FLYING EXPERIENCE: 			68 hours

All times given in this report is Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

5Y-BXQ picture after the occurrence

REMARKS

The aircraft took off from Wilson Airport for circuit training in the local Training area at 1430 with the pilot as the sole occupant with 4 hours fuel endurance. The pilot requested ATC for a 60 minute flight in the local training area to perform training exercises circuits. Wilson airport was both the departure and destination aerodrome.

The pilot stated that he flew for approximately 1 hour uneventfully, having performed several “touch and gos” (landings with subsequent take offs without coming to a stop) on runway 07. While performing the intended final touch and go on runway 07, after touching down, as he  applied power for the subsequent take-off, he reported that the aircraft started veering strongly to the left. He was able to arrest the veering and the aircraft came to rest on the grass adjacent to the drainage trench on the left of runway 07, parallel to the centerline and approximately 70 metres from the intersection of runway 07 and taxiway B. The pilot reported that he performed normal shut down procedures and exited the aircraft unaided and unharmed.

ATC personnel activated the crash alarm once the aircraft exited the runway and fire and ambulance services were deployed to the site.

Preliminary examination of the aircraft did not reveal any external damage.

CHIEF INVESTIGATOR OF ACCIDENTS

04/04/ 2016