MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:					Private

AIRCRAFT TYPE:					Pitts S.2B

AIRCRAFT MANUFACTURER: 			Pitts Aerobatics, Afton, Wyoming

YEAR OF MANUFACTURE:			1985

AIRCRAFT REGISTRATION:			5Y-MBM

AIRCRAFT SERIAL NUMBER:			5076

DATE OF REGISTRATION:			14 March 2007

TYPE OF ENGINE:				1 x Lycoming IO-540

DATE OF OCCURRENCE:			23 Feb 2018

TIME OF OCCURRENCE:			1030

LOCATION OF OCCURRENCE:	Wilson Airport

TYPE OF FLIGHT:					Private Flight

NUMBER OF PERSONS ON BOARD:		Crew – 1

INJURIES:	Nil

NATURE OF DAMAGE:	Minor

CLASS OF OCCURRENCE:	Serious Incident

PIC’S FLYING EXPERIENCE: 		4700 Hours

All times given in this report are Coordinated Universal Time (UTC) East African Local Time is UTC plus 3 hours.

PHOTO

5Y-MBM after the incident

REMARKS

On 23 February 2018 at 1030 a Pitts tail dragger aircraft, registration 5Y-MBM veered off runway after landing on runway 07 at Wilson Airport. The aircraft was reported to have been on practice of aerobatics.

According to the Captain who was the sole occupant onboard, the landing was uneventful until about 200 metres after touch down when the aircraft suddenly began shaking with a shimmy vibration from the left side of the main landing gear. The aircraft departed the runway with the left main landing gear folding rearwards part way and left wing hitting the runway sign for runway 14/32. The aircraft came to rest on the grass after the intersection of runway 07/14.

The Captain vacated the aircraft uninjured.

The aircraft sustained minor damage. The right wing tip was dented to the left at the leading edge area. The left main landing gear fairing was cracked at the wheel assembly attachment point. The engine cowling was slightly punched on the left side and one of the propeller blades slightly damaged at the tip.

At the time of the serious incident the weather condition was clear visibility with broken cloud cover.

Investigations into the cause(s) of the serious incident are ongoing.

Fredrick Kabunge

Investigator –In-Charge

27-February-2018