MINISTRY OF TRANSPORT AND INFRASTRUCTURE

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION DEPARTMENT

PRELIMINARY REPORT

OPERATOR/OWNER			:	Flight Training Centre

AIRCRAFT TYPE/MANUFACTURER	: 	Cessna 172N/Cessna Aircraft Company

YEAR OF MANUFACTURE		:	1977

AIRCRAFT REGISTRATION		:	5Y-JUX

AIRCRAFT SERIAL NUMBER		:	17268154

DATE OF REGISTRATION		:	01 April 2014

NUMBER AND TYPE OF ENGINE	: 	One Lycoming O-320-H2AD

DATE OF OCCURRENCE		:	29 August 2017

TIME OF OCCURRENCE			:	1630 hours

LOCATION OF OCCURRENCE	:	Kajiado County close to African Nazarene

University (1°23’44”S, 36°47’45”E)

DEPARTURE AERODROME	:	Wilson Airport

DESTINATION AERODROME	:	Wilson Airport

TYPE OF FLIGHT				:	Training

NUMBER OF PERSONS ON BOARD	:	One

INJURIES	:	Minor

NATURE OF DAMAGE	: 	Substantial

CATEGORY OF OCCURRENCE	:	Accident

PILOT IN COMMAND			:	YK-9572-PL

PIC FLYING EXPERIENCE		:	100 hours

Times given in this report are East African Local Time

REMARKS

On 29 August 2017 at 1640 hours, the Air Accident Investigation Department (AAID) was notified of an accident by the Wilson Airport Air Traffic Control (ATC) Tower. A Cessna 172N of registration 5Y-JUX operated by Flight Training Centre crash-landed near African Nazarene University in Kajiado County following reported engine vibration and loss of power.

5Y-JUX departed Wilson Airport on 29 August 2017 at 1608 hours for a solo cross-country training flight to Amboseli and back. The pilot was a PPL holder on CPL training. Preflight checks including engine power checks were reported to have been satisfactory. Takeoff and climb were also reported to have been uneventful. At approximately 1617 hours while at an altitude of 6200 feet AMSL, the pilot reported experiencing aircraft vibrations that were followed by a change in engine sound. A drop in engine RPM was also noted by the pilot. The pilot reported engaging engine full throttle setting but there was no change in RPM or aircraft vibrations. The pilot then decided to turn back to Wilson Airport. On the way back, the aircraft continued to lose power and the pilot decided to land on a murram road close to the African Nazarene University. Just before landing, the pilot reported sighting a truck coming in the opposite direction and decided to land on a field with shrubs next to the road. The pilot also reported shutting down the engine just before touchdown. At approximately 1630 hours, the aircraft made contact with the shrubs before coming into contact with the ground. The nose landing gear and the left wing impacted the ground before the aircraft flipped over.

The aircraft sustained substantial damage on the left wing, tail and the forward section of the fuselage as a result of this occurrence. The pilot sustained minor injuries.

The investigation is in progress.

Chief Investigator of Accidents

04/09/2017